## Slide 1: MARTe Multi-Platform Real-Time executor
A. Neto, October 2014

## Slide 2: MARTe?
Multi-platform C++ real-time control middleware
  Simulink-like way of describing the problem
Modular development and execution environment for control systems
Ensures and monitors real-time
Facilitates test & commissioning

## Slide 3: Main features
Modular
Clear boundary between algorithms, hardware interaction and system configuration
Reusability and maintainability
Simulation
Agnostic of the operational environment
  Different profiles of people can develop in parallel
    Interfaces to hardware
    Algorithms
    Interfaces to CODAC
  Develop and test in different platforms
    Deploy the same source

## Slide 4: Modularity (GAMs)
Define boundaries
  Algorithms and hardware don't mix!
  Modules do only what they advertise
  No interdependence or a priori knowledge
Generic by design
  Same goals, same module
  Reusability and maintainability
Simulation
  Replace actuators and plants with models
  Keep all the other modules untouched
Hardware
Models
Persistence
Algorithms
Debug
Information
Scheduling
Decision

## Slide 5: Dynamic Data Buffer (DDB)
GAMs share data through a memory bus
MARTe guarantees coherency between requested and produced signals
Set of GAMs allow to stream data to different MARTe systems
  Distributed control systems

## Slide 6: Real-Time Threads
Sequentially execute GAMs
  Work as micro-schedulers
  Can be allocated to specific CPUs
Keep accurate information about execution times
Require an external time and triggering mechanism
Multiple RTThreads can run in parallel
  Synchronously or asynchronously

## Slide 7: IOGAM
Interface between GAMs and outside world
  Bridge data into/from DDB signals
    Using MARTe high level drivers
Connect to hardware
  ADCs
  DACs
  DIOs
  Networks
  Filesystems
  …

## Slide 8: External Time Triggering Service
Responsible to trigger a control cycle
  One per real-time thread
Driven by an external entity
  Clock
  ADC
  Network
  Time vector from experimental data
    Repeat past experiments

## Slide 9: Data driven components (MARTe language)
Structured syntax
  Defines common language
  Simple
    Human readable configuration
  Provides built-in validation
  Allows for a clear way of expressing the problem
Similar to XML
Classes are automatically instantiated
Configuration is validated by the created object
Asserting and parsing functions available
+HttpServer = {
Class = HttpService
Port = 8084
}
...
+Control = {
Class = ControlGAM
Controller = {
NoPlasmaVelocityGain = 0.0
NoPlasmaCurrentGain = 40.0
IPWaveform = {
Times = {0 120}
Amplitudes = {0.5 0.5}
Rounding = 50
}
...

## Slide 10: Live Introspection
Probe the system
Without sacrificing RT
Crucial for an expedite debugging
Automatically built
GAM from protection system at JET

## Slide 11: MARTe components
State machine
Driver pool
External time
triggering services
GAM 1
GAM 2
GAM N
DDB
RTThread 1
MARTe
GAM 1
GAM 2
GAM N
DDB
RTThread N

## Slide 12: Interfacing with MARTe
MARTe
HTTP Server
Logger Server
Configuration
provider
Data retrieval
facility
State machine
Any other
Object N

## Slide 13: Where is MARTe being used
JET
Vertical Stability
COMPASS
Shape control
Real-time Protection Sequencer
Vessel Thermal map
Equinox
Walls
Beta-Li
As part of post-processing codes
Vertical Stability
ISTTOK
Integrated plasma control
FTU
Integrated plasma control
Additional heating control
KSTAR
*Density control
RFX
Performance studies of the framework

## Slide 14: Why I believe MARTe is a good framework
Allows different type of users to work together
  …at the same time…
  …in the same project…
  Drive people to focus on what they know best
    GAMs
      Modelers
      Physicists
      Control engineers
      Software engineers
    IOGAMs/High level drivers
      Control engineers
      Software engineers
    Interfaces
      Software engineers

## Slide 15: Why I believe MARTe is a good framework
Truly reusable
  The same framework can run in the office and in the real-time environment
  No code changes
Portable
  Can run anywhere without any specific dependences
  No dependencies on external libraries
    That are not controlled by the community
Simple hardware interface concept
  The IOGAM/high level driver enables to very easily change the input data source(s) and the output data sink(s)
  Commission friendly
    Easily broken into smaller pieces…
    …that might be part of a bigger orchestra…