Introduction
- Elongated tokamak plasmas are susceptible to a vertical axisymmetric instability
- Dedicated Vertical Stabilisation System required
- Essential system for operation
- Growth rate of 1000s-1
- Loss of control can produce forces in the order of the 100's of tonnes

---
VS New Hardware
192 signals acquired by ADCs and transferred at each cycle
50 s control loop cycle time with jitter < 1 s
• Always in real-time (24 hours per day)
1.728 x 109 50 s cycles/day
Crucial for ITER very long pulses
192 input signals

---
VS requirements
18 GAM instances
Altogether execute in less than 40 ms
Synchronization always achieved within 0.8 ms
192 signals acquired by ADCs and transferred at each loop
Enable advanced experimental features
ELM pacing
Complex time windows with different controller features and settings

---
MARTe for the new VS
Low Jitter (<<1us)